## Slide 1
Rohit Sharma
Product Manager - Grid Connectivity
S&C Electric Company
Rohit.Sharma@sandc.com
Understanding Your Options
Methodology for Evaluation and Selection of Wireless Communication Systems for Smart Grid Applications

## Slide 2
Network Demands
High Speed
Low Delay
High Availability
Grid Applications
Network demands increase with advanced applications
AMI
Grid Automation: Rapid Self-Healing
Grid Network Control: Advanced Grid Applications

## Slide 3: Early Grid Applications
Metering
Network Demands
AMR
AMI
Demand Response
AMI Connectivity provides access to valuable data

## Slide 4: Grid Application proliferation starts
Metering
Network Demands
AMR
AMI
Demand Response
OMS
Distribution Automation
SCADA
proprietary
Protection and Switching
DMS
SCADA
DNP3
An integrated AMI/OMS can improve recovery, but it is not Automation

## Slide 5: Grid Application advancements
Shift from slow, centralized to expedient, intelligent control
Metering
Network Demands
AMR
SCADA
proprietary
Volt-Var
Protection and Switching
AMI
Demand Response
Distribution Automation
DMS
OMS
Rapid
Self-Healing
Grid Automation & Control
Enhanced
Coordination
SCADA
DNP3

## Slide 6: Grid Application proliferation
AMR
SCADA
proprietary
Volt-Var
Protection and Switching
AMI
Demand Response
DMS
OMS
Rapid
Self-Healing
Enhanced
Coordination
Video Surveillance
IEC61850
Renewable
Control
Frequency
Regulation/ PMUs
SCADA
DNP3
Metering
Network Demands
Distribution Automation
Grid Automation & Control
Future applications to automate outage reduction “Grid Automation & Control”

## Slide 7: Requirements considerations for Grid Communications
Requirement | Parameter
Bandwidth | Packet rate (pps)
 | Packet size
Quality of Service | Latency
 | Jitter
 | Packet Loss
 | Transaction delay
 | Traffic Priority
Network Management | Alarms logging
 | Statistics logging
 | Accounting
 | Privacy
 | Time Sync
Requirement | Parameter
Scalability | No. of devices
 | Packet size
 | Multicast
Availability | Uptime
 | Redundancy
 | Fault tolerance
Security | Authentication
 | Authorization
 | Confidentiality
 | Privacy
 | Integrity
 | Segmentation
 | Threat detection & mitigation

## Slide 8: Latency requirements for grid applications
Rapid Self Healing: The difference between 10msec and 1000msec results in a difference of 3 to >30 seconds
CEC: Miss the latency here, and the opportunity has been missed
Latency tolerant
Latency sensitive
Latency intolerant

## Slide 9: Grid Application demands
Application | Throughput (kbps) | Latency (msec) | Availability
AMI & Demand Response Legacy Distribution Automation (SCADA, Volt-Var, DMS, OMS) | <100 | 500 to 1000 | 2 to 3 NINES
Grid Automation & Control: Rapid Self-Healing | >100 | <100 | 4 to 5 NINES
Grid Network Control: Communication Enhanced Coordination | >300 | <80 | 5 NINES
Frequency Regulation IEC61850/GOOSE Type 1B (Load Shedding) | >500 | 10 to 50 | 5 to 6 NINES
IEC61850/GOOSE Type 1A (Transfer Trip) | >1000 | 3 to 10 | 6 NINES

## Slide 10: Public cellular networks (P2MP)
  Master connects remote stations
  Single point of failure
  Coverage and overlap issues
  Quality of Service burns channel capacity
  PSBN build-out and cost
Cellular Type | Latency (msec) | Applications
3G | 80 - 150 | Metering/Latency Tolerant Apps Legacy “DA” Slow Self Healing (limited range)
WiMAX | 50 - 110 | 
4G LTE | 40 - 100 | Moderate Speed Self Healing
Public Safety Broadband Network/Private 700 LTE | 40 – 100 | 

## Slide 11: Private mesh radio networks
    No single failure point
    Easily extensible
    Vast Performance Differences
Mesh Type | Latency (msec) | Peak Throughput (kbps) | Typical Spectrum | Applications
Legacy AMI | 100 - 700 | ~100/ node | 900MHz ISM | Metering/Latency Tolerant Apps Legacy “DA” Slow Self Healing (limited range)
Distribution Automation | 25 - 350 | ~300 | 900MHz ISM, 900 MHz Licensed | 
Grid Automation & Control Layer3 | 10 - 70 | ~650 | 900MHz ISM, 900 MHz Licensed | Rapid Self Healing Communication Enhanced Coordination
Grid Automation & Control Layer2 | 1 - 7 | > 6000 | 2.4GHz 4.9GHz 5.xGHz | Backhaul IEC61850 Type 1B/1A Future Apps (Video)
Notes: Talk about evolution of 802.154g

## Slide 12: Other aspects in choosing Communication Systems
Network ownership
  Build private network or lease public network
Cost
  CAPEX (high for private comm sys, low for cellular or satellite)
  OPEX (low for private comm sys, high for cellular or satellite)
  Financing and ROI
Coverage
  Size of area to cover – huge, large, medium, or small
  Urban, sub-urban, and rural

## Slide 13: Other aspects in choosing Communication Systems
Regional spectrum availability
Interference issues
  Mitigation using Frequency Hopping Spread Spectrum
  Use of licensed frequencies
Lifetime and Innovation
  Integration of legacy deployed systems with new technology

## Slide 14: Layered Communications approach
WAN
PLC
AMI-WAN
3G/4G
3G/4G
3G/4G
900 MHz ISM & Licensed
Grid Automation &
Control WAN
4.9 GHz
5.4 GHz
5.8 GHz
2.4 GHz
Collector
Notes: Single purpose networks not viable
Diverse use cases
No single network is sufficient
Separation into multiple, layered networks
  specialized, efficient solutions
  enables smooth migrations

## Slide 15: Conclusion
Fast, reliable, and secure communication networks are must have for success of Smart Grid
No single communications technology will fit all needs
A layered, purpose built network approach is most efficient , cost responsible, and extensible
Grid Applications are evolving and becoming more demanding on the networks that support them
Require lower latency and higher bandwidth as Grid Applications and associated Grid Automation & Control evolves

## Slide 16: Questions?
16