## Slide 1: Regenerative Braking in Mass Transit
2015 Grid of the Future Symposium
Cigre US National Committee
N. Kasza, E. A. Paaso

## Slide 2: Outline
Introduction
Theory
Brake controller
Opportunities of regenerative braking
Challenges of regenerative braking
Energy storage systems
Existing implementation
Conclusion

## Slide 3
Converted energy can be utilized immediately, stored, or sent back to the electric grid
Not new technology
Regenerative Braking
An energy recovery mechanism which slows down a vehicle

## Slide 4
Regenerative brakes initiated
*Substantially more beneficial the more a train stops
Theory
How regenerative braking works:
Reversal process: cut power to the motor
Wheels turn motor and generate power
Kinetic energy recoverable from regenerative braking:

## Slide 5
Fundamental to regenerative braking functioning properly
Remote control
Determines initiation, termination, and duration of braking
Monitors speed and calculates the torque available to generate electricity
Most imperative: determining if the motor can handle the force necessary to bring the vehicle to a halt
Brake Controller
Where TR is the rotational torque, i is the continuously variable transmission speed ratio, N is the final reduction gear ratio, TREG is the regenerative torque by the motor, 𝞰 is the generation efficiency, and W1 and W2 are weight factors

## Slide 6
Lengthened brake life: lowers maintenance and costs
Effective in AC locomotives
Opportunities For Regenerative Braking
Air Quality
Energy Efficiency
Increased energy and environmental awareness
SO2
NOx
CO2
Meet regulatory requirements

## Slide 7
Regenerative braking must be used in conjunction with other brakes
  Backup brakes in the event of failure
  Battery and capacitor charge limitations
Not 100% reliable
Still a loss of energy
Less effective in DC locomotives
Challenges for Regenerative Braking

## Slide 8
Battery Storage
Longer battery usage before recharging
Completely electric application
Energy Storage Systems
Superconducting Magnetic Energy Systems
Multiple benefits
Rarely used
Virtually unavailable for regenerative braking right now
Flywheel Energy Storage
Momentum rotation
Vehicle runs smoothly
Extra weight from heavy metal rim
Stores energy for a long time
Ultracapacitor Storage Systems
Designed small to reduce wavering
Multiple applications

## Slide 9
High speed train applications have surfaced in Japan, France, India, New Zealand, England and Germany
A Northeastern transportation company in the United States has seen a huge success from regenerative braking implementation
  $900,000 state grant and $1.44 million grant from FTA
An intercity passenger train service in the United States received 70 high-efficiency electric trains destined for routes across DC, Massachusetts, New York, and Pennsylvania
Multiple other applications in the Western United States
Existing Implementation

## Slide 10
Increased interest in regenerative braking
Technology is available and useful
Multiple benefits
Few challenges
Energy storage methods can be utilized
Conclusion

## Slide 11
Thank you!